## Slide 1
Xylo Hardware
Philipp Weidel
Neuromorphic R&D Engineer, SynSense AG

## Slide 2
Xylo HDK
USB-C bus powered
Direct interface from Python for running network on device
Bit-accurate simulation in software
Deployment from trained network in two lines of Python code
Available now

## Slide 3
Xylo Overview

## Slide 4
Xylo Neurons

## Slide 5
Limitations and Constraints
Number of neurons
  16 input channels
  1000 hidden neurons
  8 output neurons
Connectivity
  Max fan out: 64
  Avg fan out: 32
Integer arithmetic only
  Addition, Subtraction, Bitshift
  No multiplication / division
Bit-depth:
  Weights: 8 bit signed integer
  States: 16 bit signed integer
Approximated exponential decay through bitshifts

## Slide 6
Thank you ！
Contact us
QiaoNing
Founder and CEO
000 0000 0000
Make Intelligence Smarter
Follow Us